1/10
An Implementation of Dawson Integral
Under the guidance of Prof. V. Milutinovic
Presenter - Jayendra Khandare
(jkhandar@umail.iu.edu)

---
2/10
Dawson Integral[1]
- Given by function,
- As it is an odd function, it can be given as,
- For applying to the Complex plane, it can be modified as,
- where erfi(z) is error function and w(z) is Faddeeva function

---
3/10
Dawson Integral Graphical Representation
From the graph for Dawson Integral, it can be said that this function can be taken as one sided Fourier – Laplace sine transform of the Gaussian function.[2]
[Speaker Notes: Incur an overhead/cost for this reconfigurability; but can make that back by efficient architecture (dataflow)]

---
4/10
Implementation Details
- This implementation is for Maxeler Systems and works on data-flow based model.
- The base code was used from the book :
  - “ Numerical Recipes in C ” [3]
- The function can be summed up as :
                  (eq.1)
- When h is sufficiently small and n large enough,
  speedup is possible.

---
5/10
Requirements for Acceleration
- There are 6 requirements for a loop to be ported to data-flow model. [4]
- The base C code has 2 loops.
- Both of them can be accelerated since both are used
  - Multiple times hence their level of re-usability is high.
  - They contribute highly to the overall execution time.
- The first factor in (eq.1) is accelerated in this implementation.
- An outline is given for calculating the value of the third factor.
- Second factor is not calculated using a loop,
  hence it cannot be accelerated using data flow model.

---
6/10
How to run this Implementation
- This implementation is created using WebIDE [5]
  - provided by Maxeler Technologies.
- It also uses ‘simpleKernel template’ which already exists in WebIDE account.
- Simply copy the CPUcode and EngineCode into respective files.
- Change the value of x in the CPUCode to the one you desire.
- Delete all pre-existing .max configuration files[6] from :
  - CPUCode/results
  - RunRules/Simulation/maxfiles
- Press ‘BUILD’ button which will compile the code and create graphs, and DFEs.
- At the end, you will get the results as:
  - the value of F(x) which is Dawson’s Integral for the float value (x) provided before
  - the graphs created for this implementation

---
7/10
What actually happens
- During one unit of time called a tick,
- the Kernel executes a step of computation,
- consumes one input value, and
- produces one output value.
- This is done after creating appropriate graphs.

---
8/10
Graph created
for LOOP 1

---
9/10
References
1. ‘Dawson Integral’ information page maintained at
  https://en.wikipedia.org/wiki/Dawson_function
2. Graphical represenation of Dawson Integral given at
  http://www.ebyte.it/library/codesnippets/DawsonIntegralApproximations.html
3. ‘Numerical Recipes in C’ - The art of Scientific Computing Second Edition
  by William H. Press, Saul A. Teukolsky, William T. Vetterling, and Brian P. Flannery
4. Instructions provided by Prof. V. Milutinovic for porting a loop into data-flow system.
  http://home.etf.rs/~vm/os/vlsi/predavanja/maxeler.html
1. WebIDE provided by Maxeler Technologies(available free to students)
  https://maxeler.mi.sanu.ac.rs/
2. A special thanks to Mr. Ognjen Andric for providing instructions to correct a bug found in WebIDE.
  oandric@maxeler.com

---
10/10
About Presenter
- Jayendra Khandare
- Graduate Student at School Of Informatics and Computing, Indiana University Bloomington
- Created this implementation for :
  - CSCI B649 DATAFLOW SUPERCOMPUTING
- Course taken for 3 Credits
  - under Prof. V. Milutinovic